## Slide 1: Sequential Circuits

## Slide 2
What we have learned in the last lecture
  - Devices that can carry out one step of operation
• What they can’t do
  - “Remember” history of operations
  - Carry out a sequence of operations in which later operations depend on results of previous ones

## Slide 3
  • Combinational circuits
  - Outputs determined solely by inputs
  • Sequential Circuits
  - Characterized by feedbacks
  - Outputs determined by inputs and previous outputs

## Slide 4: Flip Flops
A flip-flop
- A smallest sequential circuit
- Can “remember” a bit of information
SR latch

## Slide 6: Clock Pulses/Signals
a clock signal is a particular type of signal that oscillates between a high and a low state

## Slide 7: Edge-Triggered Flip-flops
Output changes state at a specified point on a triggering input called the clock.
Change state either at the positive edge (rising edge) or at the negative edge (falling edge) of the clock signal.

## Slide 8: Clocked SR Flip Flop
When CK = 0, the value of Q does not change
When CK = 1, the circuit acts like an ordinary S-R flip-flop
S | R | Q(t) | Q(t+1) | 
0 | 0 | 0 | 0 | No change
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | Reset
0 | 1 | 1 | 0 | 
1 | 0 | 0 | 1 | Set
1 | 0 | 1 | 1 | 
1 | 1 | 0 | x | Indeterminate
1 | 1 | 1 | x | 

## Slide 9: D Flip Flop
The output terminals Q and Q’ behave just as in the S-R flip-flop.
Q changes only when the clock signal CP makes a positive transition.

## Slide 10
0 0
1
Clock
Value of D is read into the latch.
Value of D is remains in the latch.
time

## Slide 11: Uses of Flip Flops - Registers
Using D Flip Flops you can build a register which will only pass data on when the clock triggers.
D0-D7 are the data bus lines from the memory.
R0-R7 is an 8 bit register.
D
C
Q
D
C
Q
D
C
Q
D
C
Q
D
C
Q
Clock
R1
R2
R3
R4
R5
D
C
Q
D0
D1
D2
D3
D4
D5
R6
D
C
Q
D6
R7
D
C
Q
D7
R0